## Slide 1
I2C0CONSET: Set the bits
I2EN: I2c Interface Enable
STA: Start bit
STO: Stop bit
SI: Interrupt Flag (Hardware )
AA: selecting Acknowledgement bit (ACK- 1 )

## Slide 2: I2CCONCLR : Clear the bits
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
- | I2CENC | STAC | - | SIC | AAC | - | -
I2ENC: I2c Interface Disable
STA: Start bit cleared
SI: Interrupt Flag cleared
AAC: selecting Acknowledgement bit (NACK=0)

## Slide 3: I2C0STAT
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
status | I2CENC | STAC | - | SIC | - | - | -

## Slide 4: I2C0DAT: data register(txn, rxn)
fPCLK
I2Cbitfrequency = -----------------------------------------
I2CSCLH + I2CSCLL
PCLK=CCLK/VPB VPB=4
CCLK=FOSC/M
I2C0SCLL=75;
I2C0SCLH=75;
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 5: I2C Master
Enable I2C Interface bit(I2C0CONSET) .
Clock selection.
I2C0CONSET=1<<6;
I2C0SCLL=75;
I2C0SCLH=75;

## Slide 6: Start
Start bit 1.
Wait for start bit execution. (wait SI bit becomes 1).
I2CSTATUS: 0x08
I2C0CONSET=1<<5;
while(!(I2C0CONSET&(1<<3))) ;

## Slide 7: SlaveAd+Write
Load SlaveAD+Write value in I2CDAT.
Clear start bit and SI bit.(I2C0CONCLR).
I2CSTATUS
  0x18 : Slave transmitted ACK
  0x20 : Not Ack
I2C0DAT=0xD0;
I2C0CONCLR=1<<5|1<<3;
while(!(I2C0CONSET&(1<<3))) ;

## Slide 8: Data Transmission
Load data in I2CDAT.
Clear SI bit.(I2C0CONCLR).
I2C0STAT
  0x28 Data transmitted and rec ack
  0x30 Data transmitted NACK
while(!(I2C0CONSET&(1<<3))) ;
I2C0CONCLR=1<<3;

## Slide 9: Stop Communication
Stop bit 1.(I2C0CONSET)
I2C0CONSET=1<<4;

## Slide 10: I2C MASTER REC

## Slide 11: Start
Start bit 1.
Wait for start bit execution. (wait SI bit becomes 1).
I2CSTATUS: 0x08
I2C0CONSET=1<<5;
while(!(I2C0CONSET&(1<<3))) ;

## Slide 12: SlaveAd+Rd
Load SlaveAD+Read value in I2CDAT.
Clear start bit and SI bit.(I2C0CONCLR).
I2C0STAT
  0x40 ACK
  0x48 NACK
I2C0DAT=0xD1;
I2C0CONCLR=1<<5|1<<3;
while(!(I2C0CONSET&(1<<3))) ;

## Slide 13: Data Transmission (slave to Master)
Load data in I2CDAT.
Clear SI bit.(I2C0CONCLR).
Select ACK/NACK
  AA bit in I2C0CONSET for ACK
  AAC bit in I2C0CONCLR for NACK
I2C0STAT
  0x58 Data byte has been received; NOTACK has been returned
  0x50 Data byte has been received; ACK has been returned.
while(!(I2C0CONSET&(1<<3))) ;
I2C0CONCLR=1<<3;